## Slide 1
Acoustic Drone Detection System
Passive multi-layer detection • RF-fusion ready • laptop proof-of-concept
Capabilities, Range & Phased Roadmap
Prepared for Forged by Freedom • Prototype / planning document

## Slide 2
OVERVIEW
Executive Summary
• Goal: passively detect drones by their acoustic signature, with no transmissions of our own.
• Core principle: a drone is not one tone — it is a structured, persistent, modulated harmonic stack. We detect the structure, not just sound in a band.
• Five cooperating layers reject the everyday confusers (fans, leaf blowers, RC planes, HVAC, traffic, insects):
  – Harmonic stack — blade-pass fundamental + its overtones
  – Persistence — must hold for several seconds
  – Multi-rotor beat — multiple props slightly out of sync
  – RPM modulation — the tell-tale hover 'wobble'
  – Direction-of-arrival — bearing from a mic array
• Designed to fuse with a separate RF detection system: RF gives long-range early warning, acoustic confirms and catches RF-silent / autonomous drones.
• Working software prototype already validated on synthetic + recorded audio. Laptop proof-of-concept needs ~$40–110 in parts.

## Slide 3
WHY IT'S HARD
Frequency Alone Always False-Alarms
• Propeller noise overlaps heavily with:
  – Fans, HVAC, compressors
  – Leaf blowers, lawn equipment
  – RC planes / other hobby craft
  – Traffic, insects, wind
• Monitoring 'one clean band' cannot isolate drones — there is no clean band.
• The fix: require a PATTERN, not a frequency
  – steady multi-tone harmonic stack
  – repeated signature lasting seconds
  – rapid RPM modulation
  – multiple props slightly out of sync
  – directional confirmation
  – cross-check with RF / video
• Each layer a confuser must defeat simultaneously — which they almost never do.

## Slide 4
THE SIGNATURE
Acoustic Physics — Blade-Pass Frequency
• Blade-pass frequency (BPF) = the fundamental tone:
  – BPF = RPM ÷ 60 × number of blades
• Examples:
  – 2-blade @ 6,000 RPM = 200 Hz
  – 3-blade @ 6,000 RPM = 300 Hz
  – Big slow heavy-lift prop ≈ 60–250 Hz
• Then the harmonics: 2×, 3×, 4×, 5× BPF, often reaching 1–5 kHz.
• Motor/ESC whine: ~4–12 kHz (close-in only — dies fast outdoors).
• Band plan
  – Low 50–700 Hz — blade-pass + low harmonics (range workhorse)
  – Mid 700 Hz–5 kHz — harmonic stack
  – High 5–12 kHz — ESC/motor whine (short range)
• Low frequencies barely attenuate in air → they carry far. High frequencies fade within ~100 m outdoors.
• Heavy-lift = low fundamental + loud = excellent acoustic target.

## Slide 5
HOW IT WORKS
The Five Detection Layers
1 · Harmonic stack
Find a fundamental in 50–700 Hz with ≥3 overtones above the local noise floor.
2 · Persistence
Signature must reappear for ~3 s before alerting. Kills one-off transients.
3 · Multi-rotor beat
Two fundamentals a few Hz apart = multiple desynced rotors (hexa/octo).
4 · RPM modulation
Hover causes a small rapid 'wobble' in the fundamental. Steady tones do not.
5 · Direction (DOA)
Mic array + SRP-PHAT gives a bearing and rejects diffuse background noise.
Fusion-ready
Outputs structured detections for cross-checking with the RF system.

## Slide 6
PROOF OF CONCEPT
Laptop Setup — Signal Chain
USB mic (or pair)
→
Laptop audio in
→
FFT + harmonic analysis
→
5-layer logic
→
Detection + bearing
→
→ RF system fusion
• Pure-numpy analysis path runs on any modern laptop — no GPU, no cloud, no API keys.
• Validate today for $0: feed it a recorded drone flyby (YouTube → 16-bit WAV) before buying any hardware.
• Add one USB mic for live single-channel detection; add a 4-mic array for live bearing.

## Slide 7
BILL OF MATERIALS
Proof-of-Concept on a Laptop
Item
Purpose
Cost (USD)
Laptop you already own
Runs the detector (numpy). No GPU needed.
$0
Recorded drone clips → WAV
Validate the DSP before buying anything.
$0
Dayton iMM-6 (or USB MEMS mic)
Single-channel live measurement mic.
$25–60
USB mic OR ReSpeaker 4-Mic Array
4 mics = live bearing (direction).
$70 (array)
Furry windscreen / dead-cat
Mandatory outdoors — kills wind in low band.
$10–25
USB extension / tripod clip
Place mic away from laptop fan noise.
$10
TOTAL — single mic POC
Prove detection + RPM/beat layers
≈ $40–95
TOTAL — array POC (with DOA)
Adds live direction-of-arrival
≈ $90–110

## Slide 8
PERFORMANCE
Detection Range — Acoustic (night / quiet)
• Small consumer drone (~70 dB @1m):
  – Quiet rural night: ~150–300 m
  – Quiet suburban: ~80–150 m
• Heavy-lift electric + payload (~85–95 dB @1m):
  – Quiet rural night: ~0.8–1.5 km
  – Loudest builds, dead calm: ~2 km
  – Quiet suburban: ~300–700 m
• Classification range ≈ 60–70% of raw detection range.
• Range multipliers
  – Parabolic / shotgun mic: +10–20 dB in-beam → 2–3× range in that sector
  – 4-mic array beamforming: ~6 dB + noise rejection
  – Night + quiet = lowest noise floor = best case
• Range killers
  – Wind (raises low-band floor — use windscreen)
  – Terrain / obstructions

## Slide 9
PERFORMANCE
Combined with RF — Fusion Envelope
Target
Effective range (night/quiet)
Driven by
RF-emitting consumer drone
~1–3 km early warning; acoustic confirms last 150–300 m
RF
Heavy-lift, RF-emitting
RF 1–5 km + acoustic 0.8–2 km (heavy overlap)
RF + acoustic
RF-silent / autonomous drone
~150 m–2 km depending on size
Acoustic only
Fusion's payoff is confidence + coverage, not just range: a track confirmed on both modalities is high-trust and low-false-alarm, and the union means you are blind to neither the RF-silent drone (acoustic catches it) nor the distant emitter (RF catches it).

## Slide 10
HONEST LIMITS
What This Does Not Do (yet)
• Acoustic is a close-in layer, not perimeter radar — range is tens of meters to ~2 km, weather-dependent.
• Bearing from a small array is coarse at low frequency (physics, not code). A larger baseline or high-harmonic steering is needed for tight bearings.
• Multi-rotor 'beat' flag is reliable as binary; exact beat value is coarse (FFT resolution).
• Wind degrades performance fast — windscreen + siting matter as much as the mic.
• Acoustic alone will still occasionally confuse loud RC craft / equipment — that's why RF cross-check matters before acting.
• No classification of make/model yet (that's a future ML phase). Current output: 'drone-like acoustic signature, bearing X, multi-rotor yes/no.'

## Slide 11
ROADMAP
Phased Development Plan
Phase 0
Laptop POC
Validate DSP on recordings + 1 mic. $0–95.
Phase 1
Single field node
Raspberry Pi + 4-mic array, weatherproof. Live bearing. ~$180–250.
Phase 2
Directional / range node
Parabolic or shotgun mic for 2 km+ in a sector. ~$350–650.
Phase 3
Multi-node network
3+ nodes triangulate position, not just bearing. Mesh / LoRa backhaul.
Phase 4
RF + acoustic fusion
Unified track table; correlate RF DF with acoustic bearing.
Phase 5
ML classification + cueing
Train classifier on signatures; auto-slew a PTZ camera to bearing.

## Slide 12
FUTURE
Expansion Opportunities
• Sensing
  – ML signature classifier (make/model/payload-state)
  – High-harmonic DOA for tight bearings
  – Optical / IR camera slewed to acoustic bearing
  – Rotor-count + RPM estimation from beat structure
• System
  – Multi-node TDOA → true GPS position + track
  – Unified fusion dashboard with RF DF
  – Mesh / LoRa backhaul for remote nodes
  – Alerting: SMS / app / siren / log
  – Solar + battery for off-grid perimeter nodes

## Slide 13
BUDGET
Indicative Cost by Phase
Phase
What you get
Indicative cost
0 · Laptop POC
Prove the detection works
$0–95
1 · Single node
24/7 field node, live bearing
$180–250
2 · Directional node
Long-range (2 km+) sector coverage
$350–650
3 · 3-node network
Position/triangulation
~$700–1,500
4 · RF fusion
Software integration (uses existing RF kit)
Mostly dev time
5 · ML + cueing
Classification + camera slew
Dev + ~$150–600 optics
Costs are indicative hobby/prototype pricing, USD; exclude labor. Confirm current part prices before purchase.

## Slide 14
ACTION
Recommended Next Steps
• 1. Validate for $0 — run the detector against 3–5 recorded heavy-lift drone clips. Confirm it locks the harmonic stack + flags multi-rotor.
• 2. Buy the single-mic POC kit (~$40–95) and test live against a known drone at measured distances to calibrate real-world range.
• 3. Add the 4-mic array to bring up live bearing; tune band weighting for your specific heavy-lift fleet.
• 4. Define the fusion interface to the RF system (shared track format, time-sync).
• 5. Decide Phase 1 siting — where the field node lives, power, and backhaul.
• Software prototype (drone_detect.py) is attached and already tested.